THERMODYNAMICS  OF  SURFACE  TENSION  AND  CALCULATION OF  CONSTANTS  OF  EQUATION  OF  EötvöS

V.P. Barabanov,  D.N. Kolushev, D.M. Torsuyev,  M.A. Khusainov

Kazan State Technological University

K.Marx St., 68, Kazan, 420015, Russia

E-mail: : kolushevdn@kes.tatenergo.ru

The constraint equation of power constants [1] allows to take into account the associative interactions in liquids not being represented in the equation of Eötvös [2]:

, , S=2/3 ± h

The thermodynamic constant КЕ  [erg/deg] characterizes the influence of temperature on variation of molar volume of liquid and represents the work doing against the forces of surface tension in the process of heating at one degree. The constants КЕ obtained differ from the known classical values of КЕ, as they take into account according to h the degree of molecular associations not being represented by the classical equation. The «constant» КЕ, as also the masses of associates Мass, of certain liquids depend on temperature. They may increase, decrease or remain invariable. The actual values of the constants allow to calculate the values of temperature in the point of parachore of a liquid making use of the equation:

where Рa is  the paraсhore;

γ is  the surface tension equal to 1.

Given in the table are the constants and points of parachore of different liquids

| Liquid | К20е | К50е | КЕ20 | КЕ50 | М | Мass | Mass/M | TP | TC | ∆TP |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| о-xylene | 2.18 | 2.21 | 18.88 | 19.38 | 106 | 2706 | 25.5 | 612 | 631 | 19.1 |
| μ-xylene | 2.19 | 2.18 | 2.36 | 2.36 | 106 | 119 | 1.12 | 597 | 617 | 22.2 |
| p-xylene | 2.18 | 2.17 | 2.86 | 2.86 | 106 | 160 | 1.50 | 595 | 616 | 20.7 |
| о-toluidine | 2.26 | 2.28 | 13.26 | 13.52 | 107 | 1524 | 14.2 | 676 | 694 | 18.0 |
| μ-toluidine | 2.08 | 2.12 | 101.7 | 106.0 | 107 | 36703 | 342.5 | 689 | 709 | 20.0 |
| p-toluidine | 2.40 | 2.38 | 5.51 | 5.51 | 107 | 374 | 3.5 | 648 | 669 | 18.6 |

The nature of variation of constant КЕ in the process of heating corresponds to the variation of the degree of association, being indicative of the degree of stability of the associate.

LITERATURE

[1] XVIII-th Mendeleyev congress on general and applied chemistry. М., 2007. v.1, p.117. V.P. Barabanov, D.N. Kolushev, D.M. Torsuyev, M.A. Khusainov. Power constants of equations of Van-der-Waals, McLeod-Sagden and Eötvös as criteria of surface and associative interaction in liquids of different nature

[2] R.C. Reid, T.K. Sherwood. The properties of Gases and liquids. McGRAW-HILL BOOK COMPANY, New York  San Francisco  Toronto  London  Sydney, 1966