SURFACE PROPERTIES OF MULTICOMPONENT SYSTEMS WITH THE CENTRAL INTERMOLECULAR INTERACTIONS

L.R. Minibayeva, A.V. Klinov, S.G. Dyakonov

Kazan state technological university

Russia, 420015,. Kazan, street. K.Marks, 68, minibayeva@kstu.ru

The algorithms are developed and created the computation program complex of surface properties of multicomponent systems with the central intermolecular interactions by a method of Monte-Carlo on algorithm Metropolis. The liquid film in equilibrium with a vapor phase in a rectangular cell by the sizes X×Y×Z was simulated, where Z = 3X = 3Y. The adequacy of the developed algorithms was calibrated by comparison calculation results of the surface tension for Lennard-Jones fluid with the available data of other authors.

Are carried out research of behaviour of a profile of density and surface tension coefficient on vapor – liquid interface for:

- fluids with differently central potentials of interaction (Buckingham and power potential);

- two-component Lennard-Jones systems, depending on the characteristics of potentials of intermolecular interaction of components of a mix.

Was revealed, that the value of a surface tension for single-component systems with various potentials of intermolecular interaction depends on a form of function, with which the repulsion is described.

The calculations have shown, that the value of a surface tension in binary Lennard-Jones mixes appears low-sensitive to the sizes of molecules of components and strongly depends from energy of their attraction.

The work is executed at support RFBR, grant № 08-08-00590-а.