EXPERIMENTAL INVESTIGATION OF THE PHASE BEHAVIOR OF HYDROCARBONS  IN FREE VOLUME AND IN POROUS MEDIA

Buleiko V.M.1, Voronov V.P.2

1VNIIGAS, Moscow, Russia, 2OGRI RAS РАН, Moscow, Russia

V_Buleiko@ vniigaz.gazprom. ru

The results of experimental investigations of the phase behavior both of hydrocarbon  mixtures (ternary, binary) and pure hydrocarbons in a free volume, in dry and water-saturated porous media have been presented. Experiments have been performed in VNIIGAZ by the experimental complex consisted of two high-resolution adiabatic calorimeters constructed in accordance with the specificity of the problems to be solved.

The first calorimeter is destined for studying fluids in a free volume, while the second calorimeter is meant for investigations in a porous medium. “Principle of comparison” in the experimental system is realized. Experimental properties of fluid measured in balk are compared with those confined in porous media. The studies are carried out within the pressure range of 0.1-60 MPa and temperature range of  78-425 К with an error  0,0005 К and 0,0007 MPa, respectively [1].

The results of our experiments showed that because of the sorption both the quantitative and qualitative transformations of the fluid phase behavior occur.

Sorption of hydrocarbons occurs as the result of peculiarities of the porous medium skeleton, of the water-saturation of porous media and of composition of the hydrocarbon fluid [2].

The results of experimental investigations of the influence of the water-saturation of the porous media on sorption and desorption of hydrocarbons have been presented.

REFERENCES

1. V.M.Buleiko. “Porous media implications for phase behavior of gas/condensate mixtures” . Gazovaya promishlennost. 1 (2007) 22.

2. V.M.Buleiko, V.P.Voronov, S.N.Zakirov, E.S.Zakirov, and I.M.Indrupskii. “Regularities in the Behavior of Hydrocarbon Systems of Oil and Gas Pools”. Doklady Earth Sciences. 415(5) (2007) 686