NUMERICAL MODELLING OF DECIDUOUS TREE IGNITION BY GROUND LIGHTNING DISCHARGE TAKING INTO ACCOUNT MOISTURE EVAPORATION

1,2N.V. Baranovsky, 2G.V. Kuznetsov

1Research institute of applied mathematics and mechanics of Tomsk State University, Russia, 634050, Tomsk, Lenin av., 36. E-mail: firedanger@narod.ru

2Tomsk Politechnic University, Russia, 634050, Tomsk, Lenin av., 30

Course of an electric current in a trunk of deciduous and coniferous trees is various [1]. Transport of a moisture at trees of deciduous breeds is carried out in a massive central part [1]. It is supposed, that in various sections of a trunk the electric current has identical parameters. It is considered, that evaporation of a moisture can be described by Knudsen-Langmuir equation [2]. As a result of electric current course current occurs having warmed up wood due to Joule heat and at achievement of critical heat flows to a surface of ignition and critical temperature there is an ignition of a tree. It is supposed, that formed pore space is filled by steam.

Ignition limits of a tree trunk during action of the electric discharge are established at various voltage and force of a current. At force of a current less than 15 кА and a voltage 1 - 50 кV there is no ignition during action of a ground lightning discharge (duration of action 500 ms) [3].

REFERENCES

[1] K.Ezau. Anatomy of seed plants. The book 1. Mir, Moscow, 1980.

[2] V.M.Pankratov, Ju.V.Polezhaev, A.K.Rudko Interaction of materials with gas streams. Mashinostroenie, Moscow, 1975.

[3] C.P. Burke, D.L. Jones. On the polarity and continuing current in unusually large lightning flashes deduced from ELF events. Journal of Atmospheric and Solar-Terrestrial Physics. 58 (1996) 531.