TERMODYNAMIC PROPERTIES OF HYDROCARBON

MULTICOMPONENT MIXTURES NEAR THE

LIQUID-VAPOR CRITICAL POINT

M. Yu. Belyakov, V.P. Voronov, E.E. Gorodetskii, and V.D. Kulikov

Oil&Gas Research Institute of the RAS, Russia,119333 Moscow, Gubkina str. 3

e-mail: gorod@ogri.ru

Phase behavior and temperature dependencies of pressure and isochoric heat capacity  in the neighborhood of the liquid-vapor critical point in the hydrocarbon ternary mixture (methane +0.35 mol.fr. of propane +0.15 mol.fr. of pentane) have been studied by means of high-precise adiabatic calorimetry. The temperature dependence of pressure has been investigated for ten different isochores in the density range 0.1850.444 g/cm3. The heat capacity  was measured for four near-critical isochores. It has been shown experimentally that in mixtures along with the anomaly of isochoric heat capacity  the anomaly of the derivative  takes place in contrast to one-component fluids. A general approach for the description of physical properties of multicomponent mixtures in the vicinity of their critical points based on transformation of experimental variables to some special variables has been developed [1]. The proposed approach enables us to describe quantitatively all the data obtained in the experiment. The suggested approach does not depend on the number of the components in mixture and in this sense it appears to be universal.

# LITERATURE

[1] M. Yu. Belyakov, V.P. Voronov, E.E. Gorodetskii, and V.D. Kulikov. JETP Letters 88 (2008) 302